## Slide 1: Storage Device
Xin Liu
Operating Systems
COP 4610

## Slide 2: Disk as An Storage Device
An old storage technology
  Invented in the 50s
Incredibly complicated

## Slide 3: Disk Characteristics
Disk platters: coated with magnetic materials for recording
Disk platters

## Slide 4: Disk Characteristics
Each disk platter is divided into concentric tracks
Disk platters
Track

## Slide 5: Disk Characteristics
Disk arm: moves a comb of disk heads
  Only one disk head is active for reading/writing
Disk platters
Disk arm
Disk heads
Track

## Slide 6: Disk Characteristics
A track is further divided into sectors. A sector is the smallest unit of disk storage
Disk platters
Disk arm
Disk heads
Track
Sector

## Slide 7: Disk Characteristics
A cylinder consists of all tracks with a given disk arm position
Disk platters
Disk arm
Disk heads
Track
Sector
Cylinder

## Slide 8: Disk Characteristics
Cylinders are further divided into zones
Disk platters
Disk arm
Disk heads
Track
Sector
Cylinder
Zones

## Slide 9: Disk Characteristics
Zone-bit recording: zones near the edge store more information (higher bandwidth)
Disk platters
Disk arm
Disk heads
Track
Sector
Cylinder
Zones

## Slide 10: Hard Disk Trivia…
Aerodynamically designed to fly
  As close to the surface as possible
  No room for air molecules
Therefore, hard drives are filled with special inert gas
If head touches the surface
  Head crash
  Scrapes off magnetic information

## Slide 11: More About Hard Drives Than You Ever Want to Know
Track skew: starting position of each track is slightly skewed
  Minimize rotational delay when sequentially transferring bytes across tracks
Thermo-calibrations: performed to account for changes of radius due to temperature changes
Typically 100 to 1,000 bits are inserted between sectors to account for minor inaccuracies

## Slide 12: Disk Access Time
Seek time: the time to position disk heads (~4 msec on average)
Rotational latency: the time to rotate the target sector to underneath the head
  Assume 7,200 rotations per minute (RPM)
  7,200 RPM / 60 min/sec= 120 RPS
  1/120 RPS = ~8 msec per rotation
  Average rotational delay is ~4 msec

## Slide 13: Disk Access Time
Transfer time: the time to transfer bytes
  Assumptions:
    300 Mbytes/sec
    4-Kbyte disk blocks
  Time to transfer a block takes 0.07 msec
Disk access time
  Seek time + rotational delay + transfer time

## Slide 14: Disk Performance Metrics
Latency
  Seek time + rotational delay
Bandwidth
  Bytes transferred / disk access time

## Slide 15: Examples of Disk Access Times
If disk blocks are randomly accessed
  Average disk access time = ~8 msec
  Assume 4-Kbyte blocks
  4 Kbyte / 8 msec = ~500 Kbyte/sec
If disk blocks of the same cylinder are randomly accessed without disk seeks
  Average disk access time = ~4 msec
  4 Kbyte / 4 msec = ~ 1 Mbyte/sec

## Slide 16: Examples of Disk Access Times
If disk blocks are accessed sequentially
  Without seeks and rotational delays
  Bandwidth: 300 Mbytes/sec
Key to good disk performance
  Minimize seek time and rotational latency

## Slide 17: Disk Tradeoffs
Assumes 1,000-bit paddings between sectors
Larger sector size  better bandwidth
Wasteful if only 1 byte out of 1 Mbyte is needed
Sector size | Space utilization | Transfer rate (data / time)
1 byte | 8 bits/1008 bits (0.8%) | 125 bytes/sec (1 byte / 8 msec)
4 Kbytes | 4096 bytes/4221 bytes (97%) | 500 Kbytes/sec (4 Kbytes / 8 msec)
1 Mbyte | (~100%) | 300 Mbytes/sec (peak bandwidth)

## Slide 18: Disk Controller
Few popular standards
  IDE (integrated device electronics)
  ATA (advanced technology attachment interface)
  SCSI (small computer systems interface)
  SATA (serial ATA)
Differences
  Performance
  Parallelism

## Slide 19: Disk Device Driver
Major goal: reduce seek time for disk accesses
  Schedule disk request to minimize disk arm movements

## Slide 20: Disk Arm Scheduling Policies
First come, first serve (FCFS): requests are served in the order of arrival
  + Fair among requesters
  - Poor for accesses to random disk blocks
Shortest seek time first (SSTF): picks the request that is closest to the current disk arm position
  + Good at reducing seeks
  May result in starvation
  Note: SSTF is not optimal

## Slide 21: Disk Arm Scheduling Policies
SCAN: takes the closest request in the direction of travel (an example of elevator algorithm)
+ no starvation
- a new request can wait for almost two full scans of the disk

## Slide 22: Disk Arm Scheduling Policies
Circular SCAN (C-SCAN): disk arm always serves requests by scanning in one direction
  Once the arm finishes scanning for one direction
  Returns to the 0th track for the next round of scanning

## Slide 23: First Come, First Serve
Request queue: 3, 6, 1, 0, 7
Head start position: 2
Tracks
0
5
4
3
2
1
6
7
Time

## Slide 24: First Come, First Serve
Request queue: 3, 6, 1, 0, 7
Head start position: 2
Total seek distance: 1 + 3 + 5 + 1 + 7 = 17
Tracks
0
5
4
3
2
1
6
7
Time

## Slide 25: Shortest Seek Distance First
Request queue: 3, 6, 1, 0, 7
Head start position: 2
Tracks
0
5
4
3
2
1
6
7
Time

## Slide 26: Shortest Seek Distance First
Request queue: 3, 6, 1, 0, 7
Head start position: 2
Total seek distance: 1 + 2 + 1 + 6 + 1 = 10
Tracks
0
5
4
3
2
1
6
7
Time

## Slide 27: SCAN
Request queue: 3, 6, 1, 0, 7
Head start position: 2
Time
Tracks
0
5
4
3
2
1
6
7

## Slide 28: SCAN
Request queue: 3, 6, 1, 0, 7
Head start position: 2
Total seek distance: 1 + 1 + 3 + 3 + 1 = 9
Time
Tracks
0
5
4
3
2
1
6
7

## Slide 29: C-SCAN
Request queue: 3, 6, 1, 0, 7
Head start position: 2
Time
Tracks
0
5
4
3
2
1
6
7

## Slide 30: C-SCAN (always reach both ends)
Request queue: 3, 6, 1, 0, 7
Head start position: 2
Total seek distance: 1 + 3 + 1 + 7 + 1 = 13
Time
Tracks
0
5
4
3
2
1
6
7

## Slide 31: Flash Memory
A form of solid-state memory similar to ROM
  Holds data without power supply
Reads are fast
Can be written once, more slowly
Can be erased, but very slowly
Limited number of erase cycles before degradation (800 – 100,000)

## Slide 32: Physical Characteristics

## Slide 33: Grouping of SSD Cells

## Slide 34: An SSD Die

## Slide 35: An SSD Device

## Slide 36: NOR Flash
Used in cellular phones and PDAs
Byte-addressable
  Can write and erase individual bytes
  Can execute programs
Mostly replaced by DRAM + NAND flash

## Slide 37: NAND Flash
Used in smartphones, digital cameras, and thumb drives
Page-addressible
  1 flash page ~= 1 disk block (1-4KB)
  Cannot run programs
Erased in flash blocks
  Consists of 4 - 64 flash pages
  May not be atomic

## Slide 38: Writing In Flash Memory
If writing to empty flash page (~disk block), just write
If writing to previously written location, erase it, then write
While erasing a flash block
  May access other pages via other IO channels
  Number of channels limited by power (e.g., 16 channels max)

## Slide 39: Implications of Slow Erases
The use of flash translation layer (FTL)
  Write new version elsewhere
  Erase the old version later

## Slide 40: Implications of Limited Erase Cycles
Wear-leveling mechanism
  Track the number of write/erase cycles for each page
  Spread writes/erases uniformly across storage locations
Better to group writes within a block and erase together once
  Than to scatter writes to many blocks

## Slide 41: Multi-level cells
Use multiple voltage levels to represent bits

## Slide 42: Implications of MLC
Higher density lowers price/GB
Need exponential number of voltage levels to for linear increase in density
Maxed out quickly

## Slide 43: Performance Characteristics
 |  | Samsung SSD 970 Pro
Read | Latency | 2 s/4KB
 | Bandwidth | 3500 MB/s
Write | Latency | 2 s/4KB
 | Bandwidth | 2300 MB/s
Power | Active | 5.2W
 | Idle | 30 mW
Cost |  | $0.1/GB
Notes: 2018 Samsung datasheet
2021 Amazon price

## Slide 44: Pros/Cons of Flash Memory
Small and light
Uses less power than disk
Read time comparable to DRAM
No rotation/seek complexities
No moving parts (shock resistant)
Expensive (compared to disk)
Slow erase cycle (4.5ms)
Limited number of erase cycles

## Slide 45: Persistent RAM

## Slide 46: Persistent RAM
Byte-addressible
 |  | Intel Optane DC
Read | Latency | 32 ns/256B
 | Bandwidth | 6.8 GB/s
Write | Latency | 128 ns/256B
 | Bandwidth | 1.85 GB/s
Power | Active | 15W
Cost |  | $5/GB